CLANDESTINE DRUG LABS				       SOP121

GUIDELINES FOR RESPONSE TO DRUG LABS

The Vincennes Twp. Fire Department and Police Departments will be working together to deal with the chemical hazards at drug labs.

A.	Definitions:

Working Lab - This location has active chemicals, and the drug making

process is on going.  Fumes have filled the building, and may be leaving the

occupancy.  Chemical fumes may be flammable and explosive and will require

ventilation and air monitoring before entry is made.

Lab Equipment - This location contains equipment and chemicals already used,

or being stored for future use in a drug lab. This equipment may contain

dangerous chemicals left behind intentionally because those individuals did not

want to move them. These chemicals may also produce vapors, and in some

cases be shock sensitive and explode.

B.	Guidelines:

- En-route obtain wind speed and direction from dispatch, approach the scene

from the upwind side.  Park your apparatus at least 200 ft upwind from the

scene.  Start your gas detector and keep it with you. Walk to the scene and

ask for the police officer in charge of the scene. If the police have not arrived,

the first fire officer on scene is IC.

- Obtain a briefing on the incident (face to face). Size up the scene and

determine the best location to park the fire apparatus.  Consider the area

needed for setting up Entry, Decon, Medical and a separate area for

removing the chemicals from the building. Keep these areas up wind or

cross wind from the chemicals.

- Move the fire apparatus to the new location and secure the scene.  Use

yellow fire scene tape and tape off the area around the trucks and the

building.  Do not allow civilians or the news media inside this area.

- Check gas detectors for any LEL readings at exits of the building. Determine

if ventilation is required. (start ventilation if needed)

Hazmat Team firefighters will also use colormetic Drager tubes for any

suspected chemicals (ammonia, ether, etc.)

VTFD HAZMAT                                                          PAGE 39                                             UPDATED 11-21-01

- Fire Command or Operations must find the police officers at the scene

that have lab training, and will be suiting up with our firefighters.

Develop a plan for entry into the building, removing chemicals from the

building, and possibly a controlled release of some chemicals.  Make sure

that all public safety officers at the scene fully understand these plans.

- The police officers that have the DEA lab background, are trained in the

use of air packs and basic hazmat. These officers will become part of the

entry team.  Firefighters will provide air monitoring, and technical

assistance. Police will identify what items will need to be removed and

when to handle them.  Firefighters will not touch or pickup any items until

cleared to do so by law enforcement. Most lab Entry Teams will have 1

police officer and 2 firefighters.

7.  Most drug labs will usually have small amounts of chemicals and not

- require a fully encapsulating level A suit.  Normal firefighter turnout gear

- with an SCBA will provide protection. The police officer will wear a white

- level B Tyvex suit with an VTFD SCBA from Hazmat Unit.  This officer will

- be the primary person moving the chemicals.

- If a more complex lab is found during the first entry,  including acids or

poisons, the entry team must exit the building and upgrade to Level A 	suits.

- The IC may upgrade to a Level II Hazmat incident if a larger lab is found or

the chemicals require a higher level of protection. This will require a Decon,

Medical, and Rehab sectors.  An ALS ambulance will also be required at the

scene.

- Outside the building, VTFD will setup a back up team (RIT Team),  wearing

normal firefighter turnout gear with SCBA and a charged hose line at the

point of entry and exit. This team will stay up wind at the exit and ready

to assist in removing the entry team if needed.

- The hose line may be used for emergency decon. ( If Level A Suits are

used a full hazardous materials decon will also be setup)

- When ammonia is found in un-approved tanks (LP or Air tank), controlled

release should be considered. These tanks will fail. The IC should look for

an isolated area.  The release should not be close to any developed areas.

Moving small tanks in a pickup truck or van is permitted.

VTFD HAZMAT                                                                PAGE 40

13.  The controlled release should include an engine with one line set on    a  		       narrow fog pattern knocking the vapor cloud to the ground. Stay upwind.

Normal firefighter turnout gear with SCBA for protection. Occasionally

check down-wind for an ammonia odor, if ammonia can be detected apply

more GPM at the nozzle.

14. If the lab has a large inventory of chemicals needing to be removed, place a

large section of clear plastic on the ground in a safe area, big enough to

separate the different containers. Firefighters should not move any

containers until cleared to do so.

15. PD will be responsible for hazardous chemical disposal.  A cleanup

company will respond to over-pak and remove the larger items. Some

of the smaller bottles and items will become evidence.  All tanks emptied

by VTFD will return to the scene for disposal by the cleanup company.  The

police will keep a unit at the scene until the cleanup company arrives.

16. All Drager colormetic tubes used will be placed in a small plastic bag and

given to the KCPD, VPD, or ISP officer in charge for evidence.

17.  Reporting for NFIRS. Type of Situation Found - Chemical Emergency #47

VTFD HAZMAT LAB                                                PAGE 41