DECON SECTOR OFFICER		                HM109

A.     GENERAL INFORMATION

On all level I, II & III hazardous materials incidents there will be a Decon Sector, designated (Decon) appointed by the Hazmat Sector Officer. Decon shall assume responsible for establishing a decontamination site and ensuring that all personnel, clothing, and equipment are cleaned prior to their being returned to service.

B.     DECON SECTOR OFFICER FUNCTIONS

Decon sector activities shall be conducted in accordance with the following:

1.		The Decon Officer shall ensure that the decontamination

area is set up and that sufficient materials are available for

the Decon operation.

2.		Decon operations, procedures, and protective clothing shall

be coordinated with Research Information and Safety.

3.		Decon shall follow, and complete the Hazardous Materials

Decontamination Checklist.

Decontamination Procedure

Step:  1.       	Establish Decontamination Sector Area

2.	Establish Decontamination Site, Upwind, and Upgrade.

3.	Establish and mark via tape and traffic cones- HOT, WARM, and COLD zones.

4.	Place plastic sheeting on ground over entire decontamination site.  Place all Decon equipment on plastic sheeting.  Roll edges of plastic to form a dike and prevent run off.

5.	Set up tool and equipment drop off site (trash can with plastic liner)

- Set up gross decontamination area:

A.	Set up PVC shower within a run off pool

B.	Five gal. bucket w/ appropriate Decon solution

C.	Garden hose w/ nozzle

D.	Appropriate cleaning devices

E.	Plastic grating for pool

F.	Trash can w/ plastic liner

VTFD HAZMAT SOP			PAGE19				UPDATED 11-21-01

7. 	Set up final decontamination area:

A.	Set up large run off pool

B.	Five gal. bucket w/ appropriate Decon solution

C.	Garden hose w/ nozzle

D.	Appropriate cleaning devices

E.	Plastic grating for pool

F.	Trash can w/ plastic liner

8.	Set up suit removal and S.C.B.A. removal area:

A.	Chairs or bench

9.	Set up personal decontamination area:

A.	Strip down area (utilize trailer with shower or tarps)

B.	Trash can w/ plastic liner

C.	Set up portable personal shower

D.	Provide wash clothes, towels, and soap

E.	Garden hose w/ nozzle

F.	Trash can w/ plastic liner for towel disposal

G.	Tyvek clothing

10.	Set Up Medical Evaluation Area

A.	Paramedic / EMT or R.N. Staffed

B.	Medic Unit

11.	Decontamination Sector Personnel shall wear the appropriate

level of protection to be determine by the Decon Sector Officer.

DECON SOLUTIONS		                            HM109a

Solution A (Red)        1000g (2 lbs.) of NaCO3 (Sodium Carbonate) and 1000g

(2 lbs.) of Na3PO4 (Tri-Sodium Phosphate) in 5 gallons of water.

Solution B (Yellow)     2000g (4 lbs.) of HTH (Calcium Hypochlorite) in

5 gallons of water.

Solution C (Black)      1000g (2 lbs.) of Na3PO4 (Tri-Sodium Phosphate) in

5 gallons of water.

Solution D (Blue)        500g (1 pint) of concentrated HC1 (Hydrochloric Acid) in

10 gallons of water.  Use half a bottle in 5 gallons of water.

Solution E (Green)      A concentrated solution of TIDE and WATER. Mix into a paste

and scrub with brush.  Rinse with water. Add additional TIDE

and DAWN as necessary.

VTFD HAZMAT SOP			PAGE20

Known Contaminants:

The following chart should be used as a guideline for selecting degradation chemicals for the type of hazard identified.

1.		Inorganic Acids, Metal Processing Wastes 		Solution A

2.		Heavy Metals: Mercury, Lead, Cadmium, etc.  		Solution B

3.		Pesticides, Chlorinated Phenols, Dioxins & PCB’s	Solution B

4.		Cyanides, Ammonia & Non-Acidic Inorganic wastes	Solution B

5.		Solvents and Organic Compounds			Solution A or B

6.		PBB’s and PCB’s						Solution A or C

7.		Oily, Greasy Unspecified Wastes not Pesticides 	Solution C

8.		Inorganic Bases, Alkali and Caustic Wastes		Solution D

9.		Radioactive Materials					Solution E

10.		Etiologic Materials						Solution A or B

Unknown Contaminants:

The Decon solutions should be solutions of water and chemical compounds designed to react with and neutralize the specific contaminants. The temperature and contact time should also be considered to insure complete neutralization. However, the contaminants will not always be known in a majority of cases and it will be necessary to use a decon solution that is effective for a variety of contaminants.

Two of these General Decon Solutions are listed below.

1.     	Decon Solution A - A solution containing 5% SODIUM CARBONATE

and 5% TRISODIUM PHOSPHATE.  Mix two (2) pounds commercial grade

TRISODIUM PHOSPHATE with each five gallons of water

2.      Decon Solution B - A solution containing 10% CALCIUM

HYPOCHLORITE.  Mix four (4) pounds of CALCIUP HYPOCHLORITE with

Each five gallons of water.  CALCIUM HYPOCHLORITE is commonly

Known as HTH (commonly used in swimming pools).

**Caution**   The decontamination solutions listed above are recommended for the ten general groups of hazardous materials.  ALWAYS contact expert assistance from manufacturers, poison control centers, medical specialists, resource books, etc. to determine the best solution to use.

VTFD HAZMAT SOP			       PAGE 21