| Vincennes Twp. Fire Department Hazardous Materials Response Team Standard Operating Procedures | Reference No. HM – NFPA 472 |
| --- | --- |
|  | No. of Pages: 17 |
| Subject: Decontamination |
| NAME OF DECON OFFICER: | LAST UPDATE 11-21-01 |
| General Information On all level I, II & III hazardous materials incidents, a decontamination sector (designated “DECON” shall be assigned by the Hazard Sector Officer. DECON shall assume responsibility for establishing a decontamination site and ensuring that all personnel, clothing, and equipment are cleaned prior to their being returned to service. |
| DECON Functions Decon sector responsibilities and activities shall be conducted in accordance with the following: The DECON officer shall ensure that the decontamination area is set up and that sufficient materials are available for the decon operations. DECON operations, procedures, and protective clothing shall be coordinated with the Incident Commander, Tech. Support, and Safety. DECON shall follow and complete the Hazardous materials Decontamination checklist. |
| DECON Resources Containment Basins Hazmat Trailer with shower Plastic Sheeting Traffic Cones Banner Guard Tape Scrub Brushes Shower Head Applicators Garden Hoses Decon Manifold 3” Hose Blind Caps Air line and Chuck MSA SCBA Bottles Air Regulator Plastic Disposal Cans Trash Can Liners Pencil, Paper, Clipboard Hazardous Materials Decontamination Checklist |

VTFD HM / DECONTAMINATION                                                        Page 1 of 17                                                                         UPDATED 11-21-01

| DECON BRIEFING | 1. INCIDENT NAME | 2. DATE PREPARED | 3. TIME PREPARED |
| --- | --- | --- | --- |
| DECONTAMINATION PROCEDURES AND GUIDELINES 1. Never enter a clean-up site or use personal protective equipment without knowing what hazards are present and how you will exit and decontaminate. 2. Be sure you understand emergency exit and decontamination procedures before you enter a clean – up site. 3. Avoid contact with hazardous materials as much as possible. Minimize splashing, stirring up dust, etc. 4. Don’t continue working with broken, torn, or damaged protective equipment. 5. Don’t cut slits in coveralls to access your pockets. 6. Report any indication of breakthrough of respirators, gloves, coveralls to your supervisor and change equipment as instructed. 7. Follow decontamination procedures exactly as instructed. 8. Handle contaminated tools, instruments, or equipment with care. Make sure they are decontaminated properly or discarded appropriately. 9. Make sure you wash thoroughly before eating, drinking or smoking. Never eat, drink or smoke in a contaminated area. 10. Wash or shower before going home. 11. Change clothes and leave dirty work clothes in the laundry bin. 4. |
| NOTES: |

VTFD HM / DECONTAMINATION                                                           Page 2 of 17

DECON SET UP PROCEDURE 1. Establish decontamination sector. 2. Establish decontamination site, upwind and upgrade. 3. Establish and mark via tape and traffic cones; hot, warm, and cold zones. 4. Place plastic sheeting on ground over entire decontamination site. Place all decon equipment on plastic sheeting. Roll edges of plastic to form a dike and prevent run off. 5. Set up tool and equipment drop off site (trash can with plastic liner). 6. Set up gross decontamination area: Set up run off pool Five gal. Bucket with appropriate decon solution Garden hose with nozzle P.V.C. Shower Plastic grating for pool Trash can with plastic liner 7. Set up final decontamination area: Set up large run off pool Five gal bucket with appropriate decon solution Garden hose with nozzle P.V.C. Shower Appropriate cleaning devices Plastic grating for pool Trash can with plastic liner 8. Set up suit removal and S.C.B.A. removal area: Chairs or bench 9. Set up personal decontamination area: Strip down area (utilize tape) Trash can with plastic liner Set up portable personal shower Provide wash clothes, towels, and soap Garden hose and nozzle Trash can with liner for towel disposal Tyvek clothing 10. Set up medical evaluation area: Paramedic or R.N. Medic unit 11. Decontamination personnel should wear level B protection – or one level below hazard personnel. Decon sector to determine if Decon personnel should wear S.C.B.A.’s

VTFD HM / DECONTAMINATION                                                               Page 3 of 17

| HAZARDOUS MATERIALS DECONTAMINATION CHECKLIST TYPE OF INCIDENT__________________________________________ _____________________________________________________________ _____________________________________________________________ LOCATION___________________________________________________ DATE__________________________ TIME________________________ DECONTAMINATION OFFICER_______________________________ DECON PERSONNEL__________________________________________ __________________________________________ __________________________________________ __________________________________________ __________________________________________ HAZARDOUS MATERIALS INVOLVED_________________________ ______________________________________________________________ ______________________________________________________________ ______________________________________________________________ IMMEDIATE HEALTH EFFECTS OF EXPOSURES_______________ ______________________________________________________________ ______________________________________________________________ ______________________________________________________________ EFFECTS OF MATERIALS ON EQUIPMENT____________________ ______________________________________________________________ ______________________________________________________________ ______________________________________________________________ |
| --- |
| 207 ICS FORM | 6. PREPARED BY (NAME AND POSITION) |

VTFD HM / DECONTAMINATION                                                             Page 4 of 17

REACTIVITY OF MATERIALS (Check all that are applicable) MATERIALS REACTIVE WITH WATER? YES_________NO _________ MATERIALS REACTIVE WITH DECON SOLUTIONS YES_________NO_________ 1.

NOTES:

DECONTAMINATION SITE SELECTION DECON AREA LOCATED IN WARM ZONE AT EXIT FROM HOT ZONE DECON AREA LOCATED UPHILL AND UPWIND FROM HOT ZONE DECON AREA LEVEL OR SLOPED TOWARD ENTRANCE 2.

RESOURCES WATER SUPPLY ESTABLISHED DECON SOLUTION COORDINATED WITH TECH SUPPORT AND SAFETY SUFFICIENT AMOUNT OF DECON SOLUTIONS AVAILABLE PROTECTIVE AMOUNT OF DECON SOLUTIONS AVAILABLE PROTECTIVE CLOTHING COORDINATED WITH TECH INFO AND SAFETY LEVEL OF PROTECTION_____________________________________ CLOTHING TYPE___________________________________________ SUFFICIENT SCBA AND SPARE BOTTLES AVAILABLE PERSONAL SHOWERING FACILITIES ESTABLISHED ON – SITE FIXED FACILITY, SUPERVISED SHOWER SHOWER AT STATION UPON RETURN 3.

VTFD HM / DECONATAMINATION          	       	       	       Page 5 of 17

DECONTAMINATION SITE SETUP RUNOFF CONTAINED CONTAINMENT BASINS SET WITHIN CONTAINMENT AREA SHOWER HEAD APPLICATORS, GARDEN HOSES, AND MANIFOLD SET UP AND WATER FLOW ESTABLISED SUFFICIENT DISPOSAL CONTAINERS AVAILABLE AND IN PLACE FOR CLOTHING AND EQUIPMENT DROP SPARE SCBA AND BOTTLES AVAILABLE FOR DECON AND ENTRY PERSONNEL DECON SOLUTIONS MIXED ENTRY AND EXIT POINTS WELL MARKED 4.

HOT ZONE PRE-ENTRY CHECKLIST DECONTAMINATION STATION DESIGNATED LOCATION ____________________ CHECK SEWERS / DRAINS NEAR DECON STATION HAZARDOUS MATERIAL(S) IDENTIFIED CHEMICAL INFORMATION RESOURCES CHECKED DECONTAMINATION PROCEDURES DETERNIMED SUITS YES______________NO____________ EQUIPMENT YES______________NO____________ SKIN / BODY YES______________NO____________ EMERGENCY YES______________NO____________ DECON TEAM PROTECTIVE EQUIPMENT SELECTED CLOTHING YES_____________NO____________ RESPIRATORY YES_____________NO____________ GLOVES YES_____________NO____________ BOOTS YES_____________NO____________ ALL DECON / CLEANING EQUIPMENT IN POSITION DECON TEAM IN PROTECTIVE GEAR ENTRY TEAM BRIEFED ON DECON PROCEDURES

VTFD HM / DECONTAMINATION                                                             Page 6 of 17

DECONTAMINATION PROCEDURES PERSONNEL ENTER DECON AREA DROP TOOLS ON DIRTY SIDE REMOVE CONTAMINANTS STEP INTO BASIN CONFIRM THAT ENTRY PERSONNEL ARE OK ON AIR SUPPLY PROTECTIVE CLOTHING EXAMINED FOR BREACHES SCRUB CONTAMINATED PERSONNEL 6.

REMOVE / REPLACE SCBA OPEN SUIT DISCONNECT SCBA MASK WHILE PERSONNEL HOLDING BREATHING TUBE. INSERT BREATHING TUBE INTO NEW REGULATOR 7.

REMOVE PERSONAL CLOTHING REMOVE DUCT TAPE AND / OR BANDS UNZIP PROTECTIVE CLOTHING AND TURN INSIDE OUT UNDRESS ENTRY CREW PLACE CONTAMINATED CLOTHING IN DISPOSAL CONTAINERS 8.

REMOVE PERSONAL CLOTHING REMOVE UNDERGRARMENTS AND SHOWER DRY OFF REDRESS INTO CLEAN CLOTHING MEDICAL / EMS EVALUATION 9.

VTFD MH / DECONTAMINATION                                                          Page 7 of 17

| TERMINATION PROCEDURES DISPOSABLE MATERIALS ISOLATED, BAGGED, AND PLACED IN PLASTIC CONTAINERS ALL CONTAINERS SEALED, MARKED, AND ISOLATED ALL EQUIPMENT CLEANED AND ACCOUNTED FOR DOES ANY EQUIPMENT REQUIRE ISOLATION FOR FURTHER ANALYSIS OR DECONTAMINATION? YES__________NO__________ HAS ALL CONTRACTOR EQUIPMENT BEEN DECONTAMINATED? YES__________NO_________ DECON PERSONNEL CLEANED ALL ENTRY PERSONNEL CLEANED DECON SOLUTIONS CONTAINED / DISPOSED REPLENISH SUPPLIES TERMINATED DECON OPERATIONS, REPORT TO INCIDENT COMMANDER TIME_______________________ 10. |
| --- |
| NOTES |
| 207 ICS FORM | 11. PREPARED BY (NAME AND POSITION) |

VTFD HM / DECONTAMINATION                                                        Page 8 of 17

DECON SOLUTIONS Solution A (Red) 1000g (2 lbs.) of NaC03 (Sodium Carbonate) and 1000g (2 lbs.) Of Na3P04 (Tri-Sodium Phosphate) in 5 gallons of water. Solution B (Yellow) 2000g (4 lbs.) of HTH (Calcium Hypochlorite) in 5 gallons of water. Solution C (Black) 1000g (2 lbs.) of Na3P04 (Tri-Sodium Phosphate) in 5 gallons of water. Solution D (Blue) 500g (1 pint) of concentrated HC1 (Hydrochloric Acid) in 10 gallons of water. Use one- half a bottle in 5 gallons of water. Solution E (Green) A concentrated solution of TIDE and WATER. Mix into a paste and scrub with brush. Rinse with water. Add Additional TIDE and DAWN as necessary.

KNOWN CONTAMINANTS: The following chart should be used as a guideline for selecting degradation chemicals for the type of hazard identified. Inorganic Acids, Metal Processing Wastes Solution A Heavy Metals: Mercury, Lead, Cadmium, etc. Solution B Pesticides, Chlorinated Phenols, Dioxins & PCB’s Solution B Cyanides, Ammonia & Non-Acidic Inorganic wastes Solution B Solvents and Organic Compounds Solution A or B PBB’s and PCB’s Solution A or C Oily, Greasy Unspecified Wastes Non-Pesticides Solution C Inorganic Bases, Alkali and Caustic Wastes Solution D Radioactive Materials Solution E Etiologic Materials Solution A & B

VTFD HM / DECONTAMINATION                                                              Page 9 of 17

UNKNOWN CONTAMINANTS: The Decon solutions should be solutions of water and chemical compounds designed to react with and neutralize the specific contaminants. The temperature and contact time should also be considered to insure complete neutralization. However, the contaminants will not always be known in a majority of cases and it will be necessary to use a decon solution that is effective for a variety of contaminants. Two of these General Decon Solutions are listed below 1. Decon Solution A A solution containing 5% SODIUM CARBONATE and 5% TRISODIUM PHOSPHATE. Mix two (2) pounds commercial grade TRISOIDUM PHOSPHATE with each five gallons of water. 2. Decon Solution B A solution containing 10% CALCIUM HYPOCHLORITE. Mix four (4) pounds of CALCIUM HYPCHLORITE with each five gallons of water. CALIUM HYPOCHLORITE is commonly known as HTH (commonly used in swimming pools). **Caution** The decontamination solutions listed above are recommended for the ten general groups of hazardous materials. ALWAYS contact expert assistance from manufacturers, poison control centers. Medical specialists, resource books, etc. to determine the best solution to use.

VTFD HM / DECONTAMINATION                                                           Page 10 of 17

| CHEMICAL ENCAPSULATING SUITS |
| --- |
| TYPE I CHEMICAL ENCAPSULATING SUITS (SCBA INSIDE SUIT) ADVANTAGES_________________ OFFERS MAXMIUM LEVEL OF PROTECTION TO THE USER. POSITIVE INTERNAL PRESSURE MAY HELP SEAL MINOR LEAKS. IF SELF-CONTAINED BREATHING APPARATUS (SCBA) MALFUNCTIONS, THE USER MAY HAVE SOME TIME TO REACH A NON-HOSTILE ENVIRONMENT DISAVANTAGES_______________ REDUCED MOBILITY AND VISIBILITY, WITH SOME PROBLEMS IN CONFINED SPACE OPERATIONS NO EASY METHOD OF RESUPPLYING AIR CYLINDERS-MUST DECONTAMINATE BEFORE OPENING THE SUIT. PROBLEMS IN IMPLEMENTING SCBA EMERGENCY PROCEDURES. HIGHER WEIGHT THAN SIMILAR TYPE II SUITS | TYPE II CHEMICAL ENCAPSULATING SUITS (SCBA OUTSIDE SUIT) ADVANTAGES_________________ GREATER COMPORT AND MOBILITY THAN TYPE I SUITS BECAUSE OF THE CLOSE-FITTING CUT. AIR CYLINDERS CAN BE REMOVED OR CHANGED WITHOUT OPENING THE SUIT. TURNOUT COAT OR LIMITED-USE GARMENT CAN BE WORN OVER THE SUIT FOR ADDED PROTECTION DISAVANTAGES_______________ SCBA EXPOSED TO THE ATMOSPHERE WITHOUT PROTECTION FACEPIECE COMPATIBILITY (LENS AND MASK) MAY NOT BE EQUIALENT TO SUIT COMPATIBILITY. TYPE II SUITS MAY VOID THE NIOSH APPROVAL OF THE SCBA. | TYPE III CHEMICAL ENCAPSULATING (AIRLINE HOSE SUPPLIED) ADVANTAGES_________________ PERMITS EXTENDED OPERATIONS POSITIVE PRESSURE ALWAYS MAINTAINED IN THE SUIT. AIRLINGE HOSE PROVIDING A MECHANISM FOR COOLING DISAVANTAGES_______________ LIMITED MANEUVERABLILTY DISTANCE IS LIMITED TO THE LENGTH OF THE AIRLINE HOSE (GENERALLY NOT GREATER THAN 300 (FEET) PROBLEMS IN ASCERTAINING REMAINING AIR PRESSURE UNLESS A COMMUNICATION SYSTEM IS PROVIDED CONSTRUCTION OF THE AIRLINE HOSE IN REGARD TO CHEMICAL COMPATIBILITY |

VTFD HM / DECONTAMINATION                 		        Page 11 of 17

LEVEL B SUITS OR TURN OUT GEAR Page 1 You will need two garden hoses; one for each rinse and wash / rinse station. You need at least two 5-gallon pails for the Decon Solutions at each wash station. The nature of the product and level of contamination will determine the brushes to use as well as the Decon Solution. On severe to extremely toxic chemicals use the utility scrub brushes marked number 1. On moderate exposure to very little contamination use the soft bristle scrub brushes marked with duct tape. It is optional whether you hook it up to the garden hose. One use of the manifold for the garden hose, you may want to hook it up to the pump with low to no idle of the pump, or run it off a 1’ or 2’ line from the hydrant or pump. The 5-gallon buckets will contain Decon Solution for the specific categories of chemicals that you have. The swimming pools can be inflated by use of the airgun in the Decon kit. All galvanized tubs should be lined with trash bags. The husky scrub brushes with handles can be used for boots and gloves for scrubbing if needed depending on level of contamination. Long handled sponges can be used for decon of victims so decon personnel can keep a safe distance. Sponges are to be used for showering by personnel along with the use of surgical soap. Always place Decon upwind and upgrade of incident. On all decon area, place plastic sheeting down with absorbent pads underneath, from the wash and rinse stations up to the suit removal station, if enough available you might want to place sheeting under entire decon area. Make sure to place sheeting under shower stations, roll up sheeting to form dike and contain product. You might need to roll it up using duct tape. Clear plastic sheeting is main runner. Additional sheeting can be used if needed for placing next to stations for tubs, or for PVC showers, but make sure you roll up sides and ends to prevent runoff. Place traffic cones on sides of plastic sheeting and mark off with yellow tape the designate Decon area which begins at the tool drop and ends at the medical evaluation station, starts at the end of the Hot Zone through the Warm Zone and ends at the beginning of the Cold Zone.

VTFD HM / DECONTAMINATION 			         Page 12 of 17

LEVEL B SUITS OR TURN OUT GEAR Page 2 After placing sheeting down for Level B, follow the Decon procedures as to station placement and placement of pools and other equipment. When placing sheeting down designate clean side and dirty side. To avoid confusion, assume anything on the left side is clean and anything on the right side is contaminated. This will be standard for all incidents. Next to wash pools you may want to place additional pools or tubs in case you need to pump off water from wash or rinse pools to avoid overfilling and overflowing. Use Bilge pumps for the purpose. There will be a plastic or wood grate to stand on in the pools to avoid standing in . contaminated water If you have turn out gear that is contaminated place in trash bag with name of person and type of chemical exposure. At suit removal have firefighter doff. Turnout gear while leaving face piece on then proceed to SCBA removal. For tool drop always use a trash bag lined trash can and our tub for contaminated tools. Decon personnel will use Saranex / Tyvek suit for protection with SCBA. Inner glove is optional but needs to be Latex examination gloves. Always wear double gloves preferably triple gloving for Decon. (Neoprene or Nitrile rubber) Always remove jewelry, rings, before donning gloves. PVC showers should be designed so they will fit into the 52” x 10” inflatable pools. Decon personnel will Decon each other. The last person will Decon himself. Advise personnel that there will be times when they will have to be in same level of protective equipment as Entry Team. At termination of decon sector, leave everything where it is and if possible place tarp over contaminated area. You will need about two Decon personnel for each wash / rinse station and two for suit removal and SCBA removal, one for field wash, and clothing change. Make sure after the Chemfab wash / rinse that the suits are dried off using disposable towels before opening them up.

VTFD HM / DECONTAMINATION   			        Page 13 of 17

| DECONTAMINATION PROCEDURES CONTAMINATION TOOLS AND FOR LEVEL B SUITS & TURNOUT GEAR EQUIPMENT DROP ENTER TOOLS HOT ZONE |
| --- |
| CLEAN SIDE STEP 1 STEP 2 INFLATE 2 ½ “ FIRE HOSE WITH AIR AROUND PLASTIC CLEAN SIDE STEP 3 WARM ZONE STEP 4 (SHOWERS MAY BE OPTIONAL DEPENDING ON PRODUCT INVOLED) STEP 5 TRAILER with SHOWER | PVC SHOWER HERE! POOL POOL SUIT REMOVAL SCBA REMOVAL | DIRTY SIDE PRIMARY RINSE LEVEL B SUITS SARANEX / TYVEK 1 HOSE AND NOZZLE CAN BE USED WASH / RINSE LEVEL B SUITS SARANEX / TYVEK. 5 GAL. PAIL OF DECON SOLUTION WITH BRUSHES 2 GARDEN HOSES FOR POOLS TRASH CAN PLASTIC BAG LINED DISPOSABLE SUITS / BOOT DROP INNER GLOVE REMOVAL LEAVE FACEPIECE ON WHILE DOFFING SUIT TUBS FOR SCBA’S DIRTY SIDE 2 GARDEN HOSES FOR SHOWERS TRASH CAN PLASTIC BAG LINED INNER CLOTHING REMOVAL AND DROP FIELD WASH AND CLOTHING CHANGE SHOWER USING OF SURGICAL SOAP AND SPONGES PUT ON CLEAN HOSPITAL CLOTHING TRASH CAN PLASTIC BAG LINED DROP FOR CLEANING ITEMS SPONGES AND TOWELS |
| EXIT STEP 6 MEDICAL EVALUTION COLD AND TREATMENT AS ZONE NECESSARY * DECONTAMINATION SECTOR SHOULD BE IN PLACE PRIOR TO ENTRY |

VTFD HM / DECONTAMINATION			         Page 14 of 17

| DECONTAMINATION PROCEDURES CONTAMINATED TOOLS AND FOR LEVEL B SUITS & TURNOUT GEAR EQUIPMENT DROP ENTER TOOLS HOT ZONE |
| --- |
| CLEAN SIDE STEP 1 STEP 2 INFLATE 2 ½ “ FIRE HOSE WITH AIR or WATER AROUND PLASTIC STEP 3 WASH / RINSE LEVEL A SUITS STEP 4 WARM ZONE STEP 5 CLEAN SIDE STEP 6 (SHOWERS MAY BE OPTIONAL DEPENDING ON PRODUCT INVOLVED) | POOL PVC SHOWER HERE! GROSS RINSE POOL SCRUB POOL FINAL RINSE SUIT REMOVAL SCBA REMOVAL | DIRTY SIDE TRASH CAN PLASTIC BAG LINED OVERGLOVE REMOVAL AND DROP GROSS RINSE LEVEL A SUITS 1 HOSE AND NOZZLE CAN BE USED AT EACH STATION 5 GAL. PAIL OF DECON SOLUTION WITH BRUSHES 2 GARDEN HOSES FOR POOLS TRASH CAN PLASTIC BAG LINED DISPOSABLE SUITS / BOOT DROP INNER GLOVE REMOVAL LEAVE FACEPIECE ON WHILE DOFFING SUIT DIRTY SIDE TUBS FOR SCBA’S 2 GARDEN HOSES FOR SHOWERS TRASH CAN PLASTIC BAG LINED DROP FOR CLEANING ITEMS SPONGES AND TOWELS |
| COLD ZONE EXIT TRASH CAN PLASTIC INNERCLOTHING REMOVAL STEP 7 MEDICAL EVALUATION AND DROP AND TREATMENT AS FIELD WASH AND CLOTHING NECESSARY CHANGE SHOWER USING TRAILER SURGICAL SOAP AND SPONGES SHOWER PUT ON CLEAN HOSPITAL CLOTHING * DECONTAMINATION SECTOR SHOULD BE IN PLACE PRIOR TO ENTRY |

VTFD HM / DECONTAMINATION			    Page 15 of 17

| AIR SUPPLY REPORT | 1. INCIDENT NAME | 2. DATE PREPARED | 3. TIME PREPARED |
| --- | --- | --- | --- |
| INCIDENT EXPOSURE RECORD |
| NAME / SUIT # | TIME ON AIR / PSI | TIME OFF AIR / PSI | TOTAL | REMARKS |
| 1. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 2. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 3. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 4. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 5. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 6. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 7. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 8. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 9. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 10. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| MAXIMUM working times for ENTRY TEAM MEMBERS shall be determined by weather conditions and type of breathing apparatus selected, as follows: A. 30 Mins. SCBA – 15 Mins. B. 60 Mins. SCBA – 30 Mins. |
| 209 ICS FORM | 5. PREPARED BY (NAME AND POSITION) |

VTFD HM / DECONTAMINATION 		  	       Page 16 of 17

DECON OPTIONS REVIEW / DISCUSSED WET DRY WHAT ARE THE OBJECTIVES? 1.____________________________________________________________________________ 2.____________________________________________________________________________ 3.____________________________________________________________________________ 4.____________________________________________________________________________ 5.____________________________________________________________________________ V. DECON PROCEDURES REVIEW (Initial DECON SETUP) SUPPORT PERSONNEL DESIGNATED FOR EACH POOL DECON TEAM FOLLOWING AND COMPLETING CHECKLIST HAZARD AND PROCEDURES BRIEFING COMPLETED TIME_______ REVIEW ASSIGNMENT TIME_______ 10.

REVIEW EMERGENCY SIGNALS (HAND, AUDIBLE) HAND GRIPPING THROAT – OUT OF AIR – CAN’T BREATHE GRIP PARTNER’S WRIST OR BOTH HANDS AROUND WRIST - LEAVE AREA IMMEDIATELY -NEED ASSISTANCE TOUCH OPEN HAND ON TOP OF HEAD – SITUATION OK THUMBS UP – ARM RAISED – OK, I AM ALRIGHT, I UNDERSTAND THUMBS DOWN – ARM STRAIGHT OUT– NO, NEGATIVE ARMS CROSSED ABOVE HEAD – IN TROUBLE – NEED HELP – SEND BACKUP TEAM 11.

REVIEW EMERGENCY ESCAPE PLAN REVIEW SUIT / SCBA FAILURE PROCEDURES REVIEW DECON PROCEDURES ENTRY COORDINATED READY WITH DECON EMERGENCY WARNING SIGNAL KNOWN BY ALL OPERATING PERSONNEL 12.

VTFD HM / DECONTAMINATION                                                      Page 17of17

# Text boxes

VINCENNES TWP.

FIRE DEPARTMENT

Standard Operating Procedures

Hazardous Materials Team Checklist

DECON

SECTOR

Standard Operating Procedures

Hazardous Materials Team Checklist

DECON

SECTOR