| Vincennes Twp. Fire Department Hazardous Materials Response Team Standard Operating Procedures | Reference No. HM – NFPA 472 |
| --- | --- |
|  | No. of Pages: 11 |
| Subject: Entry Team |
| NAME OF ENTRY OFFICER: | LAST UPDATE 11-21-01 |
| General Information On all Level I, II, and III hazardous materials incidents, an entry sector (designated “ENTRY”) shall be assigned by the Hazard Sector Officer. ENTRY shall assume responsibility for establishing a dressing area and ensuring that all personnel, clothing, and equipment are checked prior to their being used in the HOT ZONE. |
| ENTRY Functions Entry sector responsibilities and activities shall be conducted in accordance with the following: The ENTRY Officer shall ensure that the entry dressing area is set up and that sufficient materials are available for the entry operations. ENTRY operations, procedures, and protective clothing shall be coordinated with the Incident Commander, Tech. Support, and Safety. ENTRY shall follow and complete the Hazardous Materials Entry |
| ENTRY Resources Tables for Equipment 10 Chairs Tarps for ground cover Traffic Cones Banner Guard Tape MSA SCBA Packs Radios for Each Suit Used Hazmat Suits (checked for chemicals used) Boots, Gloves (checked for chemicals used) Small Helmets for inside suits Medical Surveillance Equipment Equipment for Leak Control Pencil, Paper, Clipboard Hazardous Materials Entry Checklist |

VTFD HM / ENTRY TEAM 				         Page 1 of 11				                UPDATED 11-21-01

| ENTRY BRIEFING | 1. INCIDENT NAME | 2. DATE PREPARED | 3. TIME PREPARED |
| --- | --- | --- | --- |
| ENTRY GUIDELINES 1. Never enter a site or use personal protective equipment without knowing what hazards are present and how you will exit and decontaminate. 2. Be sure you understand emergency exit and decontamination procedures before you enter a site. 3. Avoid contact with hazardous materials as much as possible. Minimize splashing, stirring up dust, etc. 4. Don’t continue working with broken, torn, or damaged protective equipment. 5. Don’t cut slits in coveralls to access your pockets. 6. Report any indication of breakthrough of respirators, gloves, or coveralls to your supervisor and change equipment as instructed. 7. Follow decontamination procedures exactly as instructed. 8. Handle contaminated tools, instruments, or equipment with care. Make sure they are decontaminated properly or discarded appropriately. 9. Make sure you wash thoroughly before eating, drinking or smoking. Never eat, drink or smoke in a contaminated area. 10. Wash or shower before going home. 11. Change clothes and leave dirty work clothes in the laundry bin. |
| FINAL CHECKLIST DECON SECTOR READY TIME__________ MEDICAL SECTOR READY TIME__________ HOSPITAL AVAILABLE_______________ PHONE_______________ OEPRATIONS AND SAFETY NOTIFIED ENTRY READY TIME__________ |
| 211 ICS FORM | 4. PREPARDED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM    				         Page 2 of 11

| CHEMICAL ENCAPSULATING SUITS |
| --- |
| TYPE I CHEMICAL ENCAPSULATING SUITS (SCBA INSIDE SUIT) ADVANTAGES_________________ OFFERS MAXMIUM LEVEL OF PROTECTION TO THE USER. POSITIVE INTERNAL PRESSURE MAY HELP SEAL MINOR LEAKS. IF SELF-CONTAINED BREATHING APPARATUS (SCBA) MALFUNCTIONS, THE USER MAY HAVE SOME TIME TO REACH A NON-HOSTILE ENVIRONMENT DISAVANTAGES_______________ REDUCED MOBILITY AND VISIBILITY, WITH SOME PROBLEMS IN CONFINED SPACE OPERATIONS NO EASY METHOD OF RESUPPLYING AIR CYLINDERS-MUST DECONTAMINATE BEFORE OPENING THE SUIT. PROBLEMS IN IMPLEMENTING SCBA EMERGENCY PROCEDURES. HIGHER WEIGHT THAN SIMILAR TYPE II SUITS | TYPE II CHEMICAL ENCAPSULATING SUITS (SCBA OUTSIDE SUIT) ADVANTAGES_________________ GREATER COMPORT AND MOBILITY THAN TYPE I SUITS BECAUSE OF THE CLOSE-FITTING CUT. AIR CYLINDERS CAN BE REMOVED OR CHANGED WITHOUT OPENING THE SUIT. TURNOUT COAT OR LIMITED-USE GARMENT CAN BE WORN OVER THE SUIT FOR ADDED PROTECTION DISAVANTAGES_______________ SCBA EXPOSED TO THE ATMOSPHERE WITHOUT PROTECTION FACEPIECE COMPATIBILITY (LENS AND MASK) MAY NOT BE EQUIALENT TO SUIT COMPATIBILITY. TYPE II SUITS MAY VOID THE NIOSH APPROVAL OF THE SCBA. | TYPE III CHEMICAL ENCAPSULATING (AIRLINE HOSE SUPPLIED) ADVANTAGES_________________ PERMITS EXTENDED OPERATIONS POSITIVE PRESSURE ALWAYS MAINTANIED IN THE SUIT. AIRLINGE HOSE PROVIDING A MECHANISM FOR COOLING DISAVANTAGES_______________ LIMITED MANEUVERABLILTY DISTANCE IS LIMITED TO THE LENGTH OF THE AIRLINE HOSE (GENERALLY NOT GREATER THAN 300 (FEET) PROBLEMS IN ASCERTAINING REMAINING AIR PRESSURE UNLESS A COMMUNICATION SYSTEM IS PROVIDED CONSTRUCTION OF THE AIRLINE HOSE IN REGARD TO CHEMICAL COMPATIBILITY |

VTFD HM / ENTRY TEAM                                		        Page 3 of 11

| AIR SUPPLY REPORT | 1. INCIDENT NAME | 2. DATE PREPARED | 3. TIME PREPARED |
| --- | --- | --- | --- |
| INCIDENT EXPOSURE RECORD |
| NAME / SUIT # | TIME ON AIR / PSI | TIME OFF AIR / PSI | TOTAL | REMARKS |
| 1. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 2. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 3. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 4. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 5. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 6. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 7. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 8. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 9. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| 10. | TIME ON AIR | TIME OFF AIR | TIME IN MINS |  |
|  | PSI IN | PSI OUT | PSI USED |  |
| MAXIMUM working times for ENTRY TEAM MEMBERS shall be determined by weather conditions and type of breathing apparatus selected, as follows: A. 30 Mins. SCBA – 15 Mins. B. 60 Mins. SCBA – 30 Mins. |
| 211 ICS FORM | 5. PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 		  	                   Page 4 of 11

| HAZARDOUS MATERIALS ENTRY CHECKLIST NAME OF MEMBER_______________________________________________________________ LOCATION_______________________________________________________________________ DATE__________________________________TIME_____________________________________ PROTECTION LEVEL___________________SUIT NUMBER_____________________________ SUIT MATERIAL__________________________________________________________________ |
| --- |
| PERSONAL ITEMS REMOVED, TAGGED, AND SECURED SUIT COMPATIBILITY DOUBLE – CHECKED HAZARD AND PROCEDURES BRIEFED COMPLETED BY HAZMAT OPERATION OFFICER EMS EVALUATION COMPLETED (EMS SECTOR) TIME__________ AIR SUPPLY FULLY TOPPED OFF COMMUNICATIONS CHECKED CHANNEL__________ PROPER FACEPIECE SEAL / POSITIVE PRESSURE SCBA VISUAL CHECK OF ENTRY SUIT ALL ZIPPERS PROPERLY SECURED NO OBVIOUS SUIT DAMAGE UNDERGLOVES, OUTERGLOVES, AND FOOTWEAR ZIPPERS FULLY SEALED FINAL COMMUNICATIONS CHECK COMPLETED |
| NOTES: |
| 211 ICS FORM | PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 				     Page 5 of 11

| HAZARDOUS MATERIALS ENTRY CHECKLIST NAME OF MEMBER_______________________________________________________________ LOCATION_______________________________________________________________________ DATE__________________________________TIME_____________________________________ PROTECTION LEVEL___________________SUIT NUMBER_____________________________ SUIT MATERIAL__________________________________________________________________ |
| --- |
| PERSONAL ITEMS REMOVED, TAGGED, AND SECURED SUIT COMPATIBILITY DOUBLE – CHECKED HAZARD AND PROCEDURES BRIEFED COMPLETED BY HAZMAT OPERATION OFFICER EMS EVALUATION COMPLETED (EMS SECTOR) TIME__________ AIR SUPPLY FULLY TOPPED OFF COMMUNICATIONS CHECKED CHANNEL__________ PROPER FACEPIECE SEAL / POSITIVE PRESSURE SCBA VISUAL CHECK OF ENTRY SUIT ALL ZIPPERS PROPERLY SECURED NO OBVIOUS SUIT DAMAGE UNDERGLOVES, OUTERGLOVES, AND FOOTWEAR ZIPPERS FULLY SEALED FINAL COMMUNICATIONS CHECK COMPLETED |
| NOTES: |
| 211 ICS FORM | PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 				     Page 6 of 11

| HAZARDOUS MATERIALS ENTRY CHECKLIST NAME OF MEMBER_______________________________________________________________ LOCATION_______________________________________________________________________ DATE__________________________________TIME_____________________________________ PROTECTION LEVEL___________________SUIT NUMBER_____________________________ SUIT MATERIAL__________________________________________________________________ |
| --- |
| PERSONAL ITEMS REMOVED, TAGGED, AND SECURED SUIT COMPATIBILITY DOUBLE – CHECKED HAZARD AND PROCEDURES BRIEFED COMPLETED BY HAZMAT OPERATION OFFICER EMS EVALUATION COMPLETED (EMS SECTOR) TIME__________ AIR SUPPLY FULLY TOPPED OFF COMMUNICATIONS CHECKED CHANNEL__________ PROPER FACEPIECE SEAL / POSITIVE PRESSURE SCBA VISUAL CHECKED OF ENTRY SUIT ALL ZIPPERS PROPERLY SECURED NO OBVIOUS SUIT DAMAGE UNDERGLOVES, OUTERGLOVES, AND FOOTWEAR ZIPPERS FULLY SEALED FINAL COMMUNICATIONS CHECK COMPLETED |
| NOTES: |
| 211 ICS FORM | PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 				     Page 7 of 11

| HAZARDOUS MATERIALS ENTRY CHECKLIST NAME OF MEMBER_______________________________________________________________ LOCATION_______________________________________________________________________ DATE__________________________________TIME_____________________________________ PROTECTION LEVEL___________________SUIT NUMBER_____________________________ SUIT MATERIAL__________________________________________________________________ |
| --- |
| PERSONAL ITEMS REMOVED, TAGGED, AND SECURED SUIT COMPATIBILITY DOUBLE – CHECKED HAZARD AND PROCEDURES BRIEFED COMPLETED BY HAZMAT OPERATION OFFICER EMS EVALUATION COMPLETED (EMS SECTOR) TIME__________ AIR SUPPLY FULLY TOPPED OFF COMMUNICATIONS CHECKED CHANNEL__________ PROPER FACEPIECE SEAL / POSITIVE PRESSURE SCBA VISUAL CHECK OF ENTRY SUIT ALL ZIPPERS PROPERLY SECURED NO OBVIOUS SUIT DAMAGE UNDERGLOVES, OUTERGLOVES, AND FOOTWEAR ZIPPERS FULLY SEALED FINAL COMMUNICATIONS CHECK COMPLETED |
| NOTES: |
| 211 ICS FORM | PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 				     Page 8 of 11

| HAZARDOUS MATERIALS ENTRY CHECKLIST NAME OF MEMBER_______________________________________________________________ LOCATION_______________________________________________________________________ DATE__________________________________TIME_____________________________________ PROTECTION LEVEL___________________SUIT NUMBER_____________________________ SUIT MATERIAL__________________________________________________________________ |
| --- |
| PERSONAL ITEMS REMOVED, TAGGED, AND SECURED SUIT COMPATIBILITY DOUBLE – CHECKED HAZARD AND PROCEDURES BRIEFED COMPLETED BY HAZMAT OPERATION OFFICER EMS EVALUATION COMPLETED (EMS SECTOR) TIME__________ AIR SUPPLY FULLY TOPPED OFF COMMUNICATIONS CHECKED CHANNEL__________ PROPER FACEPIECE SEAL / POSITIVE PRESSURE SCBA VISUAL CHECK OF ENTRY SUIT ALL ZIPPERS PROPERLY SECURED NO OBVIOUS SUIT DAMAGE UNDERGLOVES, OUTERGLOVES, AND FOOTWEAR ZIPPERS FULLY SEALED FINAL COMMUNICATIONS CHECK COMPLETED |
| NOTES: |
| 211 ICS FORM | PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 				     Page 9 of 11

| HAZARDOUS MATERIALS ENTRY CHECKLIST NAME OF MEMBER_______________________________________________________________ LOCATION_______________________________________________________________________ DATE__________________________________TIME_____________________________________ PROTECTION LEVEL___________________SUIT NUMBER_____________________________ SUIT MATERIAL__________________________________________________________________ |
| --- |
| PERSONAL ITEMS REMOVED, TAGGED, AND SECURED SUIT COMPATIBILITY DOUBLE – CHECKED HAZARD AND PROCEDURES BRIEFED COMPLETED BY HAZMAT OPERATION OFFICER EMS EVALUATION COMPLETED (EMS SECTOR) TIME__________ AIR SUPPLY FULLY TOPPED OFF COMMUNICATIONS CHECKED CHANNEL__________ PROPER FACEPIECE SEAL / POSITIVE PRESSURE SCBA VISUAL CHECK OF ENTRY SUIT ALL ZIPPERS PROPERLY SECURED NO OBVIOUS SUIT DAMAGE UNDERGLOVES, OUTERGLOVES, AND FOOTWEAR ZIPPERS FULLY SEALED FINAL COMMUNICATIONS CHECK COMPLETED |
| NOTES: |
| 211 ICS FORM | PREPARED BY (NAME AND POSITION) |

VTFD HM / ENTRY TEAM 				     Page 10 of 11

ENTRY TACTICAL OPTIONS REVIEW / DISCUSSED DEFENSIVE OFFENSIVE WHAT ATE THE OBJECTIVES? 1.____________________________________________________________________________ 2.____________________________________________________________________________ 3.____________________________________________________________________________ 4.____________________________________________________________________________ IV. ENTRY PROCEDURES REVIEW (Initial SUIT ENTRY) SUPPORT PERSONNEL DESIGNATED FOR EACH SUIT ENTRY TEAM FOLLOWING AND COMPLETING CHECKLIST HAZARD AND PROCEDURES BRIEFING COMPLETED TIME_______ REVIEW ASSIGNMENT TIME_______ 10.

REVIEW EMERGENCY SIGNALS (HAND, AUDIBLE) HAND GRIPPING THROAT – OUT OF AIR – CAN’T BREATHE GRIP PARTNER’S WRIST OR BOTH HANDS AROUND WRIST - LEAVE AREA IMMEDIATELY -NEED ASSISTANCE TOUCH OPEN HAND ON TOP OF HEAD – SITUATION OK THUMBS UP – ARM RAISED – OK, I AM ALRIGHT, I UNDERSTAND THUMBS DOWN – ARM STRAIGHT OUT– NO, NEGATIVE ARMS CROSSED ABOVE HEAD – IN TROUBLE – NEED HELP – SEND BACKUP TEAM 11.

REVIEW EMERGENCY ESCAPE PLAN REVIEW SUIT / SCBA FAILURE PROCEDURES REVIEW DECON PROCEDURES ENTRY COORDINATED READY WITH DECON READY EMERGENCY WARNING SIGNAL KNOWN BY ALL OPERATING PERSONNEL 12.

VTFD HM / ENTRY TEAM                                                                    Page 11of 11

# Text boxes

VINCENNES TWP.

FIRE DEPARTMENT

Standard Operating Procedures

Hazardous Materials Team Checklist

ENTRY

SECTOR