| Vincennes Twp. Fire Department Hazardous Materials Response Team Standard Operating Procedures | Reference No. HM – NFPA 472 |
| --- | --- |
|  | No. of Pages: 9 |
| Subject: Incident Command Checklist |
| NAME OF IC: | LAST UPDATE 11-21-01 |
| General Information On all level I, II, & III, hazardous materials incidents an Incident Commander, designated (I.C.) will be dispatched. The I.C. can be any Hazmat tech. The Incident Commander can relinquish command to any Hazmat tech with equivalent rank or higher. |
| Command Functions Upon arrival at scene, notify on the radio to Central Dispatch and all incoming units, that the I.C. is in command and what fireground frequency to operate on. If the I.C. changes notify Central Dispatch by radio who is now I.C. Don I.C. vest to clearly identify who is in charge. Using an area or vehicle establish an Incident Command post (designated Command) and operating perimeter for base of operations. This area is to be clearly marked, and easily identified. All news releases handled through the VTFD Public Information Officer must first be cleared by the I.C. Appoint and Coordinate with Hazmat Operations Sector Officer for additional personnel, equipment, supplies, etc. Coordinate with other agencies on scene for additional support in their particular line of expertise. All emergency responders and their communications shall be coordinated and controlled through the Incident Commander. All outside agencies and personnel reporting to the incident scene must first report to the Incident Command Post, the Incident Commander will put in writing the name of the person, what agency they are with and what information that they have, and then contact the Hazmat Sector Officer with the information, the Sector Officer will then advise I.C. as to what area the person is to report to if any. I.C. shall designate a Safety Officer who is knowledgeable in firefighting and rescue operations, hazardous substance handling and decontamination procedures. I.C. shall follow as closely as possible the Incident Command Checklist to assure all sectors of operation and all command obligations have been addressed. When the incident has been reclassified to a cleanup, and a cleanup contractor has been notified the Incident Commander may be relieved of command, and site control can be controlled by the Hazmat Operations Sector Officer who will stay on scene with no less than (1) one engine company until cleanup company arrives. |

VTFD HM/COMMAND                                                        Page 1 of 9                                                UPDATED 11-21-01

| Vincennes Twp. Fire Department Hazardous Materials Response Team Standard Operating Procedures | Reference No. HM – NFPA 472 |
| --- | --- |
|  | No. of Pages: 9 |
| Subject: Incident Command Checklist |
| NAME OF IC: | LAST UPDATE 11-21-01 |
| TYPE OF INCIDENT ______________________________________________ LOCATION _____________________________________________________ DATE _________________________ TIME ___________________________ HAZMAT OPERATION OFFICER ___________________________________ 1. |
| INCIDENT COMMANDER IDENTIFIED BY VEST HAZMAT OPERATIONS IDENTIFIED BY VEST TEAM PERSONNEL ASSIGNED (by Operations Officer) NAME TIME Operations__________________________________ Safety ___________________________________ Research Info________________________________ Recon ____________________________________ Decon ____________________________________ Entry ____________________________________ Public Info____________________________________ Staging _____________________________________ 2. |

VTFD  HM / Command                                                                Page 2 of 9

| PERSONNEL |  |  |
| --- | --- | --- |
| NOTES 3. |

VTFD HM / Command                                                                 Page 3 of 9

ISOLATE AREA AND DENY ENTRY (Check all that are applicable) ACCESS TO FACILITY BLOCKED CONFIRM WITH OPERATIONS TIME_______ ACCESS TO BUILDING CONTROLLED BY FIRE DEPARTMENT CONFIRM WITH OPERATIONS TIME_______ ACCESS ROADWAYS AND RAMPS BLOCKED CONFIRM WITH OPERATIONS TIME_______ 4.

HAZARD AREA ISOLATED ROOM EVACUATED TIME_______ FLOOR EVACUATED TIME_______ FLOOR ABOVE AND TIME_______ BELOW EVACUATED ENTIRE BUILDING / TIME_______ FACILITY EVACUATED 5.

ISOLATION DISTANCES – HOT AND WARM ZONES ESTABLISHED OBTAIN FROM INFORMATION - ADVISED ALL SECTORS TIME______ EVACUATION OF EXPOSEURES REQUIRED? YES______NO_______ BASED ON SITUATION – OBTAIN DISTANCES FROM TECH SUPPORT ADVISED OPERATIONS / LAW LIAISON TIME_______ 6.

BUILDING HVAC SYSTEM – SHOULD IT BE SHUTDOWN? YES____NO____

TEAM LEADER AND SAFETY ADVISED OF THE HOT AND WARM ZONES EVACUATION DISTANCES TIME_______

TRAIN TRAFFIC STOPPED – CONFIRM WITH RAIL DISPATCHER AND HAZMAT OPERATIONS TIME_______

ACCESS TO TRACKBED RESTRICTED BY RAIL POLICE CONFIRM WITH HAZMAT OPERATIONS TIME_______

INTEGRITY OF CONTAINER / RAILCARS CHECKED TIME_______

UTILITIES LOCKOUT / TAGOUT CONFIRMED TIME_______ IS THIS A CONFINED SPACE ENTRY? YES____NO____TIME_______ If yes, Implement Confined Space Checklist

VTFD HM / Command                                                                 Page 4 of 9

| STAGING AREA AND CONTROL ENTRY (Check all that are applicable) HAZMAT STAGING AREA DESIGNATED (AWAY FROM COMMAND POST) LEVEL III EQUIPMENT MANPOWER, HAZMAT TECHS TIME_______ BREATHING AIR SUPPLY UNITS TIME_______ MEDICAL SUPPORT TIME_______ 7. |
| --- |
| HAZARD AREA ELECTRIC SERVICE DE-ENERGIZED TIME_______ |
| IDENTIFY MATERIALS SHIPPING DOCUMENTS OBTAINED TIME_______ DERAILED CARS IDENTIFIED – CONFIRM NUMBERS OF RAILCARS STILL ON TRACKS AT EACH END OF THE DERAILMENT TIME_______ CONTACT WITH TRAIN CREW OR ON-SCENE REPRESENTATIVES TIME_______ 8. |
| NAME | COMPANY | ONSCENE TIME |
| MSDS AND PRE-PLANS OBTAINED TIME_______ |
| MANUFACTURER CONTACTED FOR INFORMATION ADVISE IF RESPONSE TEAM ENROUTE TIME_______ |
| OCCUPANCY / CONTENTS OF VEHICLES / INTERIOR EXPOSURES IDENTIFIED TIME_______ |
| SHIPPER CONTACTED FOR INFORMATION TIME_______ |
| LOCATION OF ANY OTHER HAZMAT IDENTIFIED TIME_______ |
| CONTENTS OF NEARBY TRUCKS, BUILDINGS, BOXCARS TANKERS, AND OTHER CONTAINERS IDENTIFIED TIME_______ 9. |
| CHEMTREC PHONE NUMBER 800-424-9300 |

VTFD HM / Command                                                                  Page 5 of 9

EVALUATE HAZARDS AND RISKS (Check all that are applicable) INTEGRITY OF INVOLVED CONTAINER CHECKED HAZARDS EVALUATED <HEALTH> TIME_______ <FLAMMABILITY> TIME_______ <REACTIVITY> TIME_______ <SPECIAL HAZARDS> TIME_______ IS THE ISOLATED AREA (HOT ZONE) ADEQUATE? TIME_______ 10.

LIKELY HARM WITHOUT INTERVENTION (ESTIMATED) YES_______ NO_______ TIME_______

FULL SCALE EVACUTION NECESSARY YES_______ NO_______ TIME_______ IF YES, ADVISE ALL SECTORS

DECONTAMINATION RECOMMENDATION OBTAINED FROM INFORMATION TIME_______

ALL SECTORS ADVISED OF CURRENT STATUS TIME_______

OPERATIONS, SAFETY, AND DECON ADVISED OF CURRENT STATUS TIME_______

IS HELICOPTER NECESSARY FOR AERIAL SURVEILLANCE?

CHOOSE PROTECTIVE CLOTHING & EQUIPMENT (Check all that are applicable) PROTECTIVE CLOTHING RECOMMENDATION OBTAINED FROM TECH INFO TIME_______

DECONTAMINATION AREA ESTABLISHED COORDINATED WITH OPERATIONS, DECON, EMS TIME_______

PERMISSION OBTAINED FROM INCIDENT COMMANDER FOR RECON OPERATIONS COORDINATED WITH OPERATIONS, SAFETY, DECON TIME_______

MONITOR RECON TEAM COMMUNICATIONS TIME_______

RECON TEAM DEBRIEFED / DATA RETRIEVED TIME_______

NOTES

VTFD HM / Command                                                                   Page 6 of 9

| COORDINATE INFORMATION (Check all that are applicable) HAZMAT TEAM BRIEFED ON CURRENT STATUS CONFIRM WITH OPERATIONS TIME_______ MEET WITH ON – SCENE REPRESENTATIVES DO THEY HAVE THE CAPABILITY OF HANDLING THE INCIDENT? TIME_______ TEAM MEETINGS CONDUCTED TACTICAL OPTIONS REVIEWED / DISCUSSED TIME_______ 12. |
| --- |
| 1. |  |
| 2. |  |
| 3. |  |
| MANUFACTURER RESPONSE TEAM AND RAILROAD OFFICIALS MET WITH TO DETERMINE THEIR PLAN OF ACTION TIME_______ INCIDENT COMMANDER ADVISED OF THE TACTICAL OPTIONS AND RECOMMENDATIONS TIME_______ FULL BRIEFING REQUESTED WITH HAZMAT TEAM, INCIDENT COMMAND STAFF, AND OUTSIDE AGENCIES / CONTRACTOR REPRESENTATIVES TIME_______ OUTLINE – OPTIONS COURSE OF ACTIONS RESPONSIBILTIES AND ROLES OF EACH GROUP 13. |
| NOTES |

VTFD HM / Command                                                                 Page 7 of 9

| CONTROL SPILLS AND STOP LEAKS (Check all that are applicable) ALL HAZMAT SECTORS / PERSONNEL PREPARED FOR OPERATIONS |
| --- |
| PERMISSION OBTAINED FROM INCIDENT COMMANDER TO COMMENCE OPERATIONS TIME_______ |
| ENTRY DECON SECTOR READY MONITOR ENTRY TEAM COMMUNICATIONS FREQ_______ COORDINATE WITH SAFETY DURING ENTRY OPERATIONS MONITOR RAILROAD OPERATIONS MONITOR ENTRY AND DECON TEAMS REHAB SCHEDULE ESTABLISHED FOR ROTATION OF WORKING HAZMAT PERSONNEL AT THE SCENE 14. |
| DECONTAMINATION (Check all that are applicable) DECON AND RESOURCE NEEDS COORDINATED DURING OPERATION – READY TO START DECON TIME_______ 15. |
| TERMINATION (Check all that are applicable) LEVEL III DEBRIEFING COMPLETED TIME_______ LEVEL II DEBRIEFING COMPLETED TIME_______ 16. |
| NOTES |
| 200 ICS FORM | 17. PREPARED BY (Name and Position) |

VTFD HM / Command                                                                Page 8 of 9

| SECTION FUNCTIONS |
| --- |
| HAZMAT OPERATIONS SECTOR OFFICER ESTABLISH INITIAL ISOLATION ZONE ESTABLISH INITIAL EVACUATION ZONE ESTABLISH INITIAL DECON ZONE RE-EVALUATE ISOLATION AND DECON ZONE ESTABLISH EMS ZONE ESTABLISH PROTECTIVE CLOTHING GUIDELINES ESTABLISH RECON TEAM COMPLETE HAZARD AND RISK EVALUATION COMPLETE BRIEFINGS CONTROL PRODUCT (IF NECESSARY) COMPLETE TERMINATION PROCEDURES (MEDICAL EVALUATIONS, CHECKLISTS, DEBRIEFING) COORDINATE WITH TEAM LEADER AND INFORMATION INFORMATION (INFO) ID MATERIALS INVOLVED ASCERTAIN HAZARDS COMPLETE WORKSHEETS BRIEF SECTOR COMMANDER COORDINATE WITH TEAM LEADER AND ALL SECTORS SAFETY CONTROL HAZARD ZONES CONTROL POSITIONING OF APPARATUS AND EQUIPMENT CONTROL HAZARD OPERATIONS PERSONNEL DEVELOP SITE SAFETY PLAN COMPLETE WORKSHEETS COORDINATE WITH TEAM LEADER, INFORMATION AND DECON RECON ACQUIRE AND CHECK PROTECTIVE CLOTHING ACQUIRE AND CHECK RECON EQUIPMENT (CLIPBOARD, PENCILS, BINOCULARS, TELESCOPE, CAMERA(S), HELICOPTER, ETC.) CHECK SCBA TAKE VITALS (EMS) COMPLETE WORKSHEET COORDINATE WITH TEAM LEADER, HAZMAT OPERATIONS, DECON INFORMATION AND EMS DECON MAKE SITE SELECTION ACQUIRE PROTECTIVE CLOTHING | SET UP SHOWER(S), SOLUTION DISPOSAL CONTAINERS, RUN – OFF CONTROL COORDINATE WITH SAFETY RECORD DECONNED PERSONNEL AND EQUIPMENT COMPLETE CHECKSHEET COORDINATE WITH TEAM LEADER, INFORMATION AND EMS RESOURCES PROVIDE: RESEARCH MATERIALS COMMUNICATIONS EQUIPMENT PROTECTIVE CLOTHING MONITORING AND DETECTION DEVICES APPROPRIATE HAND / POWER TOOLS CONTROL EQUIPMENT EXTINGUISHING AGENTS NEUTRALIZING AGENTS ABSORBENTS / DIKING MATERIALS DECON SUPPLIES COORDINATE WITH TEAM LEADER, HAZMAT OPERATIONS, RECON / ENTRY, INFORMATION AND EMS ENTRY CHECK CHARTS / WORKSHEETS ACQUIRE PROTECTIVE CLOTHING CHECK SCBA TAKE VITALS (EMS) CHECK PROTECTIVE SUIT VERIFY COMPATIBILITY SEAL SUIT CHECK COMMUNICATIONS EQUIPMENT COMPLETE CHECHLIST COORDINATE WITH TEAM LEADER HAZMAT OPERATIONS, DECON AND INFORMATION EMS MAKE SITE SELECTION ESTABLISH TREATMENT / TRANSPORTATION AREAS (WHEN NECESSARY) PROVIDE PROTECTIVE CLOTHING ESTABLISH FIELD – TO – HOSPITAL PHONE / RADIO LINK SUPERVISE EMS OPERATIONS PROVIDE LITTER BEARERS PROVIDE EMS SUPPLIES SUPERVISE PATIENT TRANSPORT COORDINATE WITH TEAM LEADER AND INFORMATION |

VTFD HM / Command                                                                 Page 9 of 9

# Text boxes

NFPA 704

VINCENNES TWP.

FIRE DEPARTMENT

Standard Operating Procedures

Hazardous Materials Team Checklist

INCIDENT

COMMANDER