| Vincennes Twp. Fire Department Hazardous Materials Response Team Standard Operating Procedures | Reference No. HM – NFPA 472 |
| --- | --- |
|  | No. of Pages: 8 |
| Subject: SAFETY #1 or COMMAND SAFETY |
| NAME OF SAFETY #1 | LAST UPDATE 11-21-01 |
| General Information (Designated Safety #1 or COMMAND SAFETY 1. The COMMAND Safety officer works directly with the Incident Commander and reports to him on safety concerning the entire incident site. He will be in constant radio communication with Hazmat Operations Sector, OPERATIONS Safety Officer will work with Hazmat Sector Officer, Research / Information Officer, and Tech Advisor, concerning changing weather and chemical conditions affecting the overall site. Using information he has received from other sectors, or situations that have been Observed, he has the AUTHORITY TO TERMINATE (or suspend) the incident operations at any time. |
| On all Level II or III hazardous materials incidents, a safety officer (designated “SAFETY #1) shall be assigned by the Incident Commander. SAFETY shall assume responsibility for ensuring that safe and accepted practices are adhered to throughout the course of the emergency. SAFETY is also responsible for the welfare of all persons operating in the Cold and Warm Zones. |
| SAFETY Functions Safety sector responsibilities and activities shall be conducted in accordance with the following: The Safety Officer (designated “SAFETY #1) shall be positioned in the Cold Zone at the entry point into the Warm Zone. Entry into the Warm Zone shall be restricted to hazardous materials trained personnel and individuals possessing particular knowledge of the problem and situation. SAFETY #1 shall follow and complete the Hazardous Materials Safety Checklist. SAFETY #1 shall remain in constant contact with the Incident Commander, and the Hazard Sector Officer. SAFETY RETAINS AUTHORITY TO HALT OPERATIONS AND ORDER PERSONNEL BACK TO THE COLD ZONE, IF UNSAFE CONDITIONS ARE OBSERVED. |

VTFD HM / SAFETY #1                                                               Page 1 of 8                                                                 	    UPDATED 11-21-01

| SAFETY BRIEFING | 1. INCIDENT NAME | 2. DATE PREPARED | 3. TIME PREPARED |
| --- | --- | --- | --- |
| III. SAFETY RESOURCES Hazardous Materials Safety Checklist Binoculars, Telescope Clipboard, Pencil Portable Radio Watch, Stopwatch Fire Line Tape Appropriate Protection Clothing SCBA – If necessary |
| TYPE OF INCIDENT ________________________________________________________________________________________________________________________________________________________________________ OVERALL SITE SAFETY SAFETY OFFICER IDENTIFIED BY VEST POSITIONING OF COMPANIES AND PERSONNEL EVALUATED EVACUATION / ISOLATION ZONES CLEARLY MARKED TIME_______ HAZARD ZONE ESTABLISHED AND COMMUNICATED TO OPERATIONS SECTOR TIME_______ COMMAND POST AND OPERATIONS IN SAFE LOCATION TIME_______ STAGING IN SAFE LOCATION TIME_______ EVALUATE WIND SPEED AND DIRECTION TIME_______ SECURITY OFFICER DESIGNATED AND POSTED – IF NEEDED IS THE SITUATION CHANGING YES_______NO_______TIME_______ YES_______NO_______TIME_______ YES_______NO_______TIME_______ WHAT ARE THE IMMEDIATE EXPOSURES? PEOPLE _____________________ PROPERTY _____________________ ENVIRONMEMT _____________________ |

VTFD HM / SAFETY #1                                                                      Page 2 of 8

SIGNS AND SYMPTOMS SIGNS / SYMPTOMS OF EXPOSURE COMMUNICATED TO ALL INVOLVED PERSONNEL ________________________________________________________________ 2._________________________________________________________________ 3._________________________________________________________________ 4._________________________________________________________________ 5._________________________________________________________________

NOTES

VTFD HM / SAFETY #1                                                                          Page 3 of 8

| GENERAL HAZARDOUS MATERIALS BEHAVIOR MODEL |
| --- |
| EVENT (CIRCLE ALL THAT APPLY) |
| STRESS | BREACH | RELEASE |
| THERMAL MECHANICAL CHEMICAL IRRADIATION ETIOLOGICAL | DISINTEGRATION RUNAWAY CRACKING ATTACHMENTS OPEN UP PUNCTURES SPLITS / TEARS | DETONATION VIOLENT RUPTURE RAPID RELIEF SPILL OR LEAK |
| ENGULF | IMPINGE | HARM |
| CLOUD PLUME CONE STREAM IRREGULAR DEPOSITS | SHORT TERM MEDIUM TERM LONG TERM | THERMAL RADIATION ASPHYXIATION TOXIC CORROSIVE ETIOLOGIC MECHANICAL |
| NOTES: |

VTFD HM / SAFETY #1                                                                        Page 4 of 8

| GENERAL HAZARDOUS MATERIALS BEHAVIOR MODEL |
| --- |
| EVENT INTERUPTION PRINCIPLES (CIRCLE ALL THAT APPLY) |
| INFLUENCE APPLIED STRESSES | INFLUENCE BREACH SIZE | INFLUENCE QUANTITY RELEASED |
| REDIRECT IMPINGEMENT SHIELD STRESSED SYSTEM MOVE STRESSED | SHELL CONTENT LIMIT STRESS LEVEL ACTIVATE VENTING DEVICES | CHANGE CONTAINER POSITION MINIMIZE PRESSURE DIFFERENTIAL CAP OFF BREACH |
| ENGULF | IMPINGE | HARM |
| INITIATE CONTROLLED POSITION ERECT DIKES OR DAMS DILUTE | PROVIDE SHIELDING BEGAN EVACUATION | RINSE OFF CONTAMINATION INCREASE DISTANCE FROM SOURCE PROVIDE SHIELDING |
| NOTES: |

VTFD HM / SAFETY #1                                                                               Page 4 of 8

TABLE 1.1

HAZARDOUS MATERIALS DEFINITIONS

The following definitions have been abstracted from the Code of Federal Regulations, Title 49-Transportation, Parts 100 to 199.  Refer to the referenced sections for complete details.

NOTE:  Rulemaking proposals are outstanding or are contemplated concerning some of these definitions.

| HAZARD CLASS | DEFINITIONS |
| --- | --- |
|  | An Explosive – Any chemical compound, mixture, or device, the primary or common purpose of which is to function by explosion, i.e., with substantially classified in Parts 170 – 189 (Sec 173.50) |
| CLASS A EXPLOSIVE | Detonating or otherwise of maximum hazard. The nine types of Class A explosives are defined in Sec. 173.53. |
| CLASS B EXPLOSIVE | In general, function by rapid combustion rather than detonation and include some explosive devices such as special fireworks, flash powders, etc. Flammable hazard. (Sec. 173.88) |
| CLASS C EXPLOSIVE | Certain types of manufactured articles containing Class A or Class B explosives, or both, as components, but in restricted quantities, and certain types of fireworks, Minimum hazard. (Sec. 173.100) |
| BLASTING AGENTS | A material designed for blasting which has been tested in accordance with Sec. 173.114a(b) and found to be so insensitive that there is very little probability of accidental initiation to explosion or of transition from deflagration to detonation. (Sec. 173.114a(a) |
| COMBUSTIBLE LIQUID | Any liquids having a flash point above 100º and below 200ºF. as determined by tests listed in Sec. 173.115)d). Exceptions to this are found in Sec. 173.115(b) |
| CORROSIVE MATERIAL | Any liquids or solid that causes visible destruction of human skin tissue or a liquid that has a corrosion rate on steel. (See Sec 173.240 (a) and (b) for details). |
| FLAMMABLE LIQUID | Any liquid having a flash point below 100ºF as determined by test listed in Sec. 173.115(d). Exceptions are listed in Sec. 173.115(a) |
|  | Pyrophoric Liquid – Any liquid that ignites spontaneously in dry or moist air at or below 130ºF (Sec. 173.115©) |
|  | Compressed Gas – Any material or mixture having in the container an absolute pressure exceeding 40 psia at 70ºF., or a pressure exceeding 104 psia at 130ºF or any liquid flammable material having a vapor pressure exceeding 40 psia at 100ºF (Sec 173.300(b) |
| FLAMMABLE GAS | Any compressed gas meeting the requirements for lower flammability limit, flammability limit range, flame projection, or flame propagation criteria as specified in Sec. 173.300(b). |
| NONFLAMMABLE GAS | Any compressed gas other than a flammable compressed gas. |
| FLAMMABLE SOLID | Any solid material other than an explosive, which is liable to cause fires through friction, , retained heat from manufacturing or processing, or which can be ignited readily and when ignited burns so vigorously and persistently as to create a serious transportation hazard (Sec. 173.150) |

VTFD HM / SAFETY #1                                                                         Page 6 OF 8

| HAZARD CLASS | DEFINITIONS |
| --- | --- |
| ORGANIC PEROXIDE | An organic compound containing the bivalent 0-0 structure and which may be considered a derivative of hydrogen peroxide where one or more of the hydrogen atoms have been replaced by organic radicals must be classed as an organic peroxide unless – (See Sec. 173.151(a) for details). |
| OXIDIZER | A substance such as chlorate, permanganate, inorganic peroxide, or a nitrate, that yields oxygen readily to stimulate the combustion of organic matter. (See Sec. 173.151) |
| POISON A | Extremely Dangerous Poisons – Poisonous gases or liquids of such nature that a very small amount of the gas, or vapor of the liquid, mixed with air is dangerous to life (Sec 173.326) |
| POISON B | Less Dangerous Poisons – Substances, liquids, or solids (including pastes and semi-solids), other than Class A or irritating materials, which are known to be so toxic to man as to afford a hazard to health during transportation; or which, in the absence of adequate data on human toxicity, are presumed to be toxic to man (Sec 173.343) |
| IRRITATING MATERIAL | A liquid or solid substance which upon contact with fire or when exposed to air gives off dangerous or intensely irritating fumes, but not including any poisonous material, class A, (Sec 173.381) |
| ETIOLOGIC AGENT | An “etiologic agent” means a viable micro – organism, or its toxin which causes or may cause human disease. (Sec. 173.386) (Refer to the Department of health, Education and Welfare Regulations, Title 42, CFR, 72.25© for details.) |
| RADIOACTIVE MATERIAL | Any material or combination of materials that spontaneously emits ionizing radiation, and having a specific activity greater than 0.002 microcuries per gram. (Sec 173.389). NOTE: See Sec 173.389(a) through (l) for details. |
|  | ORM-A, B, C, D, or E (Other Regulated Materials) – Any material that does not meet the definition of a hazardous material, other than a combustible liquid in packaging having a capacity of 110 gallons or less, and is specified in Sec. 172.101 as an ORM material or that possesses one or more of the characteristics described in ORM-A through D below. (Sec 173.500) NOTE: An ORM with a flash point of 100ºF., when transported with more than 110 gallons in one container shall be classed as a combustible liquid. |
| ORM-A | A material which has an anesthetic, irritating, noxious, toxic or other similar property and which can cause extreme annoyance or discomfort to passengers and crew in the event of leakage during transportation. (Sec. 173.5009b)(1). |
| ORM-B | A material (including a solid when wet with water) capable of causing significant damage to a transport vehicle from leakage during transportation. Materials meeting one or both of the following criteria are ORM-B materials: (I) A liquid substance that has a corrosion rate exceeding 0.250 inch per year (IPY) on aluminum (nonclad 7075-t6) at a test temperature of 130ºF. An acceptable test is described in NACE Standard TM-01-69, and (ii) Specifically designated by name in Sec. 172.101 (Sec. 173.500(b)(2) |
| ORM-C | A material which has other inherent characteristics not described as an ORM-A or ORM-B but which make it unsuitable for shipment, unless properly identified and prepared for transportation. Each ORM-C material is specifically named in Sec. 172.101 (Sec. 173.500(b)(4) |

VTFD HM / SAFETY #1                                                                           Page 7 of 8

| RADIO TRAFFIC | 1. INCIDENT NAME | 2. DATE PREPARED | 3. TIME PREPARED |
| --- | --- | --- | --- |
| MILITARY TIME 4. COMMUNICATIONS LOG PAGE OF |
| 201 ICS FORMS | 5. PREPARED BY (NAME AND POSITION) |

VTFD HM / SAFETY #1                                                                            Page 8 of 8

# Text boxes

VINCENNES TWP.

FIRE DEPARTMENT

Standard Operating Procedures

Hazardous Materials Team Checklist

SAFETY # 1